## Slide 1
Zhen Liu
Research on NVM (I)
Cloud native relational database: PolitDB
Ruan, Chaoyi, et al. "Persistent Memory Disaggregation for Cloud-Native Relational Databases." Proceedings of the 28th ACM International Conference on Architectural Support for Programming Languages and Operating Systems, Volume 3. 2023.

## Slide 2: Disaggregated cloud-native database and PM
Backgroud

## Slide 3: Disaggregated cloud-native database
Two-tier architecture (storage disaggregation)
  compute and storage separation
    Amazon Aurora[SIGMOD’17]
    Microsoft Socrates[SIGMOD’19]
    Alibaba PolarDB[FAST’20]
Socrates Architecture
Aurora Architecture

## Slide 4: Disaggregated cloud-native database
Three-tier architecture (memory disaggregation)
  separate compute node (CN) and memory node (MN)
    PolarDB-serverless[SIGMOD’21]
    LegoBase[VLDB’21]
  Compute node: CPU+DRAM
    SQL server
    Local cache
    Committed log
  Memory node: DRAM
    Remote cache
  Storage node: SSD/HDD
    WAL Log
    Data Pages
Sample three-tier disaggregated cloud-native DB architecture

## Slide 5: PM
Multi-fold benefits to database systems
  large capacity
  low latency
  byte addressability
  persistence
Alter the landscape of the storage hierarchy
  DRAM
  PM
  SSD
  HDD
Performance-price of fast and ultra-fast storage devices(ASPLOS’23)

## Slide 6: Constraints in DRAM disaggregation and Existing PM disaggregation work shortage
Analysis

## Slide 7: Constraints in DRAM disaggregation
DRAM limited per-machine density
  one DIMM slot can hold 512GB Optane PM, but only 128GB DDR4 DRAM
DRAM volatility
  need WAL log to guarantee persistence
Write remain slow with transactions
  need to persist changes in time to the storage layer

## Slide 8: PM disaggregation: AsymNVM
AsymNVM: An Efficient Framework for Implementing Persistent DataStructures on Asymmetric NVM Architecture [ASPLOS'20]
Advantage
  share NVM resources
  base on one-side RDMA
    front-end nodes close to 100% CPU usage
    back-end nodes generate very small CPU usage (<10%)
Shortage
  focus on supporting native data structures, not universal
  heavy remote CPU usage

## Slide 9: PM disaggregation: Clover
Disaggregating Persistent Memory and Controlling Them Remotely: An Exploration of Passive Disaggregated Key-Value Stores [ATC’20]
Advantage
  scaleable PM resources
  RDMA
    low lantency
    low CPU usage
  Separate data and metadata and manage them in different forms
Shortage
  focus on simple applications (KV stores), not universal
  make the PM/network bandwidth more bottleneck-prone

## Slide 10: PilotDB Architecture and Workflow
Architecture

## Slide 11: Architecture
3-level architecture for cloud-native relational DBs
  Compute node (CN)
    SQL/TXN server
    LBP(local buffer pool)
  Persistent memory node (PMN)
    CDLog store(committed log)
    RBP(remote buffer pool)
  Storage node (SN)
    Data pages
PilotDB architecture

## Slide 12: Workflow
Transaction execution workflow
  access the LBP
    LBP: cach the most recently used data pages
    at a latency of∼0.91μs
  LBP miss, contact PMN to fetch the target page
    RBP: cach much more data pages than LBP
    at a latency of∼8μs
  RBP miss, fetch the page from SN, send another copy to RBP
    at a latency of∼277μs
  CN collect log and flush them to PMN CDLog
  PMNs evict colder pages to SN
PilotDB transaction execution workflow

## Slide 13: PilotDB major challenges
Design

## Slide 14: Challenge 1: PM bandwidth contention
PM have lower bandwidth than DRAM
  Max IOPS (R/W)
    Intel Persistent Memory 200 series (NVDIMM): 1.9M/560K
    16GB DDR-4 DIMM (2133 MT/s) (RAMDisk): 1.8M/1.4M
High PM bandwidth demands to remote PM, especially for writes
  load pages
  log WAL entries
  flush dirty pages
PilotDB design
  sends only logs to PMNs
    manage and control logs at the CN side
    ship to and apply logs at the PMN side
    update PM-buffered pages by logs

## Slide 15: Challenge 2: PM side CPU consumption
PM’s large capacity and high-density installation allow a PMN to support many tenants
PMN CPU resources could quickly become a scalability bottleneck
PilotDB design:
  make PM-side compute-light
    while still process log applications and coordinate concurrent CN access

## Slide 16: From design to implementation
Implementation

## Slide 17: CN-Driven Log
split each 16KB page into configurable, equal-sized mini-pages
  avoids read/write amplification between CNs and PMNs
PM-knowledgeable CN
  fast, RDMA-based remote PM access
  page metadata table(PMT)
CDLog
  consists of two parts:
    metadata
    data

## Slide 18: Light-Weight, RDMA-Friendly PMN Processing
Light-weight log application
  scan the WAL entries
  use DMA for memory copy
Optimistic remote read
  LBP miss, CN read the target RBP page using one-sided RDMA
  check page freshness locally

## Slide 19: Sysbench Results
Evaluation

## Slide 20: Sysbench overall performance
RO
  achieves 90.2% of the MySQL-ideal throughput
RW
  more evident advantage
WO
  throughput reach 97.0% of MySQL-ideal
  at least a 1.53× improvement over the other three baselines

## Slide 21: PM bandwidth consumption reduction
Deliver 26.4% and 59.8% higher throughput over LegoPM
Reduce remote PM write bandwidth by 40.8% and 55.5%

## Slide 22: Remote CPU involvement reduction
PilotDB
  lower number of PMN cores
  higher thoughput

## Slide 23
Thanks
May 18th, 2023